Description of file:

File "bl.prn" is an ASCII Dos file which can be imported into
most Spreadsheet software programs. The file contains
instantaneous raw data corresponding to pressures from two
transducers placed side by side (1.75 mm apart, in the lateral
direction) beneath a two dimensional boundary layer. The two
transducers were placed on a circular holder. In this case the
holder was placed on the floor of the wind tunnel and oriented
such that the transducers were aligned in a lateral direction.  

The two columns in the file correspond the two pressure signals
(i.e channel 1 and channel 2). A gain correction of G=5. has to
be applied to the data. Only the A.C component of the signal was
recorded. The respective sensitivities are for column 1 (channel
1) S1= 303. and for column 2 S2= -293. The actual pressure data
is then found through:

P1 = S1 x (Column 1) x 10 / 4096./ G /1000000.

P2 = S2 x (Column 2) x 10 / 4096./ G /1000000. 

The units of pressure are: Pascals.

For more information you can contact us at:

      The City College of New York
      Department of Mechanical Engineering
      138th street at Convent Avenue
      New York, New York 10031
      Tel (212) 650-5206

      Yiannis Andreopoulos (Professor)
      Juan H. Agui (Graduate Student)