Description of files: Each data file is on a corresponding
directory with same name. All files have a ".prn" extention and
have an ASCII Dos format which makes it possible to load the
files into most Spreadsheet software programs. 

Fig4 directory contains spectral data as appears on the Journal
paper. Files which have names of investigators contain their
data. File "full_vel" corresponds to present data at a free
stream velocity of 11 m/s. File "half_vel" corresponds to present
data at a velocity of 5.5 m/s. And file "no_vel" corresponds
present data at zero velocity (i.e. noise data). File "lpdata"
corresponds to present filtered data. File "line" corresponds to
data of reference line in figure 4 of paper marked by slopes of
-1 and -7/3. All files in this directory have the following
format: 1st column corresponds to frequency and the 2nd
corresponds to the Power Spectral densities. 

File fig8a in directory fig8a contains mean pressure coefficient
data (cp). 1st column corresponds to the radial upstream
position,on the plate, from the center of the cylinder normalized
by the cylinder diameter (i.e. r/D). The next 11 columns
correspond to the mean pressure coefficient at the following
angles (in degrees): 0,30, 45,60,80,90,100,120,135,150, and 180.

File fig8b in directory fig8b contains r.m.s of pressure
coefficient data and follows the same format as in file fig8a.
File fig9 in directory fig9 contains time scale information.  The
first column gives normalized radial position r/D. The second
column gives the corresponding Integral Time Scale. 

Files fig10a through fig10f in their corresponding directories
contains Probability Density Function (PDF) data. The format is
the same for all files. 1st column corresponds the coefficient of
pressure and the second column corresponds to the PDF.

For more information you can contact us at:

          The City College of New York
           Department of Mechanical Engineering
           138th street at Convent Avenue
           New York, New York 10031
           Tel. (212) 650-5206
  
            Yiannis Andreopoulos (Professor)
            Juan H. Agui (Graduate Student)