Description of file:

File "r74d.prn" is an ASCII Dos file which can be imported into
most Spreadsheet software programs. The file contains
instantaneous raw data corresponding to pressures from two
transducers placed side by side (1.75 mm apart) beneath a
separated flow upstream of an upright circular cylinder. The two
transducers were placed on a circular holder. In this case the
holder was placed on the floor of the wind tunnel and oriented
such that the transducers were aligned in a radial direction. 
The location of the center of the circular holder was r/D = 0.74
(r= radius from center of cylinder model,D= cylinder model
diameter).

The two columns in the file correspond the two pressure signals
(i.e channel 1 and channel 2). Column 1 corresponds to the
transducer positioned further upstream. A gain correction of G=5.
has to be applied to the data. Only the A.C component of the
signal was recorded. The respective sensitivities are for column
1 (channel 1) S1= 303. and for column 2 S2= -293. The actual
pressure data is then found through:

P1 = S1 x (Column 1) x 10 / 4096./ G /1000000.

P2 = S2 x (Column 2) x 10 / 4096./ G /1000000. 

The units of pressure are: Pascals.

For more information you can contact us at:

      The City College of New York
      Department of Mechanical Engineering
      138th street at Convent Avenue
      New York, New York 10031
      Tel (212) 650-5206

      Yiannis Andreopoulos (Professor)
      Juan H. Agui (Graduate Student)