Data for cube at Re 10^5

Files in normalized form according to:

    x ---  U direction    (main flow direction)   x=0 leading cube edge

    y ---  V direction    (height)                y=0 channel floor (foot of cube)

    z ---- W direction    (span or width)         z=0 middle or symmetry plane ( middle of cube )

    H = cube height     Ub = bulk velocity

    x,y,z  ===>  x/H, y/H, z/H

    U, V, W =====>   U/Ub, V/Ub,  W/Ub

                            2    2      2    2      2    2  
    u' , v', w'   =====>  u' / Ub  ,  v' / Ub  ,  w' / Ub  ,

    ____   ____           ____     2    ____     2  
    u'v' , u'w'   =====>  u'v' / Ub  ,  u'w' / Ub  



The following files contain, in normalized form, y,U,u^2,V,v^2,uv

*******************************************************************************************
*******N.B.******** the files *.co1 contain the data to the third order correlations      * 
*******N.B.******** the files *.co2 contain the data to the fourth order correlations     * 
********************                                                                      *
********************    These files are stored and named using the same formalism!!!!!    *
********************                                                                      *
********************       *a_.co1 or *a_.co2 indicates the second half of the profile    *
********************                                                                      *
*******************************************************************************************

  FILE          x/H     z/H   

UV1902N       -18.02     0
UV2002N       -11.44     0
UV2102N        -7.00     0
UV2102N2       -5.00     0
UV2202N        -5.00    -1.0
UV2302N        -5.00     1.0
UV2502N        -4.00     0.
UV2602N        -3.00     0.
UV2602N2       -2.00     0.
UV2702N        -1.50     0.
UV2702N2       -1.00     0.
UV2802N        -1.00     0.5
UV2802N2       -1.00     1.0
UV0103N        -0.75     0.
UV0103N2       -0.75     0.5
UV0303N        -0.75     1.0
UV1003N        -0.50     0.
UV1003N2       -0.50     0.5
UV1003N3       -0.50     1.0
UV1103N        -0.44     0.
UV1103N2       -0.42     0.
UV1203N        -0.32     0.
UV1203N2       -0.32     1.0
UV1203N3       -0.25     1.0 
UV1203N4       -0.25     0.5 
UV1303N        -0.25     0.25
UV1303N2       -0.25     0.0 
UV1503N         0.       0. 
UV1503N2        0.      -0.25
UV1503N3        0.      -0.50
UV1603N         0.      -0.54
UV1603N2        0.      -0.76
UV1603N3        0.      -1.0
UV1703N         0.      -1.5
UV1803N        -0.02    -0.5
UV2003N         0.75     0.
UV2103N         0.50     0
UV2103N2        0.50    -0.25
UV2103N3        0.50    -0.50
UV2103N4        0.50    -1.0
UV2203N         0.50    -1.5
UV2203N2        0.25     0.
UV2203N3        0.25    -0.25
UV2303N         1.0      0.
UV2303N2        1.0     -0.25
UV2303N3        1.0     -0.5
UV2403N         1.0     -1.0
UV2403N2        1.0     -1.5
UV2503N         1.08     0.
UV2503N2        1.25     0.
UV2503N3        1.25     0.25
UV2503N4        1.25     0.50
UV2603N         1.50     0.
UV2703N         1.50     0.50
UV2703N2        1.50     1.0
UV2803N         2.0      0.
UV2803N2        2.0      0.5
UV2803N3        2.0      1.0
UV2803N4        2.0      1.2
UV2903N         2.5      0.
UV2903N2        2.5      0.5
UV2903N3        2.5      1.
UV0204N         3.0      0.
UV0304N         4.0      0.
UV0404N         6.0      0.
UV0404N2        8.0      0.


The following files contain, in normalized form, y,U,u^2,W,w^2,uw

  FILE          x/H     z/H   

UW0309N        -10.8    6.0
UW0409N        -14.1    6.0
UW0409N2        -6.9    6.0
UW0609N         -0.33   6.0
UW0609N2        -6.90   0.0
UW0709N        -14.1    0.0
UW1009N         -1.0    0.0
UW1009N2       -10.8    6.0
UW1109N          0.0    3.2
UW1109N2         0.0    1.6
UW1209N          0.5    1.6
UW1209N2         1.0    1.6
UW1209N3         2.0    1.6
UW1309N          2.0    0.0
UW1609N         -0.32   0.0
UW1709N         -0.32   0.5
UW1809N          0.     1.0
UW1909N          0.48   1.04
UW2009N          1.00   1.08
UW2409N          1.50   1.04
UW2409N2         2.00   1.04
UW2509N          2.41   1.04
UW2709N          2.41   0.50
UW2809N          2.00   0.50
UW0110N          1.50   0.5
UW0410N          1.008  0.508
UW0810N          0.5    0.501
UW0611N         -0.50   0.
UW0811N         -0.50   0.5
UW0612N         -0.75   0.
UW0712N          0.     0.
UW1012N          0.50   0.
UW1212N          0.25   0.
UW1312N          0.75   0.
UW1912N          1.0    0.
UW2012N          1.08   0.
UW2412N          1.33   0.
UW0201N          1.56   0.
UW0401N          2.33   0.
UW0701N          1.24   0.48
UW0901N          0.0    0.500
UW1101N          1.25   0.25
UW1401N          1.00   0.25
UW1501N          0.5    0.25
UW1601N          0.25   0.25
UW1701N          0.     0.25
UW1801N         -0.24   0.25