This disk contains surface pressure and flowfield data of two airfoils 
obtained at Douglas Low Speed Wind Tunnel.  Parts of the data have been
published in Numerical and Physical Aspects of Aerodynamic Flows II, ed 
Cebeci, 1984, and J. Fluid Mech. Vol.160, p155, 1985.  It containes the
results of two experiments 

 Experiment 1:  Model A airfoil (chord C=24 inces) was positoned in the
tunnel test section of hight 38 inches such that the midel chord line is
aligned along the tunnel centerline (angle of attack = 0).
Freestream velocity Uref=100 fps so that Rec=6.0 million.   Boundary-layer
transition wire was placed at X/C=0.05 on the upper surface and at X/C=0.16
on the lower surface.

 Experiment 2:  Airfoil Model B (chord C=24 inches) was positioned in the
tunnel test section such that the angle of attack was 4.0 degrees and that
the point X/C=0.25 on the model chord was on the tunnel centerline.  The 
freestream velocity was same as Experiment 1.  The trip position was at 
X/C=0.05 on the upper surface and X/C=0.16 on the lower surface.

Contents of the files on this disk are:

MODEL_A.COR       MODEL A Airfoil coordinates
MODEL_B.COR       Model B Airfoil coordinates
MODEL_A.SFD       Surface pressure data of Experiment 1 with MODEl A
MODEL_B.SFD       Surface pressure data of Experiment 2 with MODEL B
MODEL_A.STD       Station data, Experiment 1 with MODEL A
MODEL_B.STD       Station data, Experiment 2 with MODEL B
MODEL_A.PTD       Pitot tube data, Experiment 1
MODEL_B.PTD       Pitot tube data, Experiment 2
MODEL_A.HWD       Hot wire data, Experiment 1
MODEL_B.HWD       Hot wire data, Experiment 2